#### PR304/Power Relays PR60 and PR80

###### Monostable and bistable power relays for commercial vehicles

Extended range of protective devices for commercial vehicles now includes power relays PR60 and PR80

Altdorf, 8.9.2008 – E-T-A Elektrotechnische Apparate GmbH, Altdorf near Nuremberg, protection specialist for on-board electrical systems, have extended their product range for commercial vehicles by the single pole monostable d.c. relay PR60 and the bistable version PR80. Typical applications will be battery isolation in trucks, buses, construction machinery and special vehicles. The relays are designed for continuous loads up to 300 A and current peaks of up to 2400 A and therefore suitable for switching huge loads, e.g. illumination equipment of harvesters, or for use in power distribution systems in construction machinery, e.g. hydraulic pumps. The relays can be operated from the driver’s cabin and protect the circuit by means of physical isolation.

The offered voltage ratings 12 V, 24 V and 48 V allow use of the relays in all types of vehicles. The terminal thread sizes M8 (100 A and 200 A) and M10 (200 A and 300 A) provide reliable connection and allow flexible wiring and running of cables in the vehicle even with large cable cross sections. A barrier between the load terminals prevents inadvertent contact of different potentials and ensures safety when bolting on.

Permanent and reliable contact to the control coil is provided by an M4 screw connection. Optionally available suppressor diodes eliminate voltage peaks which could jeopardise any control elements and which are created by the residual magnetism when switching off the control voltage.

Side mount or foot mount ensures robust installation of the relays even under harsh conditions. The enclosure provides protection class IP67 and allows installation in exposed exterior locations. The terminal area with IP00 features superior materials such as stainless steel nuts which do not affect endurance of the power relays and which are resistant against oil, fuel etc.

Caption:

Major application of the power relays PR60 and PR80 is battery isolation in commercial vehicles.

(photo: E-T-A)

E-T-A Elektrotechnische Apparate GmbH

In 2007 E-T-A Elektrotechnische Apparate GmbH achieved a total turnover of €97m and had about 1400 people on the payroll worldwide. Production, Design, Market Research and Sales are concentrated at the headquarters in Altdorf.
E-T-A’s major product line consists of circuit breakers for protection of electrical or electronic equipment against overload and short circuit. E-T-A manufactures thermal, thermal-magnetic, hydraulic-magnetic, purely magnetic and electronic circuit breakers. Solid state remote power controllers are also part of E-T-A’s product portfolio. E-T-A serves almost every industry, e.g. process control and automation, telecommunications, chemical and medical industry, manufacturers of household appliances and garden equipment, aerospace, automotive and marine industry.

For detailed information please visit E-T-A’s home page: www.e-t-a.com.

# Further information:

E-T-A Elektrotechnische Apparate GmbH

Thomas Weimann

Industriestr. 2 - 8

90518 Altdorf – Germany

Phone: +49-9187-10227

Fax: +49-9187-10448

E-Mail: Thomas.Weimann@e-t-a.de

www.e-t-a.com