# PR 286/Thermal Circuit Breaker 1120

# Thermal rocker-actuated circuit breaker for a range of electric appliances – combining performance with cost-effectiveness

# Safety with integral cost-effectiveness

The new E-T-A circuit breaker type 1120 is a combination of circuit breaker and ON/OFF rocker switch. The new breaker – particularly designed for manufacturers of electric appliances produced in high volumes – is a high-quality circuit breaker offering compact design and attractive cost-effectiveness.

Type 1120 has been designed under the motto “German superior quality at a Far-East-price” for single-phase applications and snap-in front panel mounting. Single pole and double pole versions with one pole protected are available, shortly also with additional water splash protection. It is therefore suitable for many applications such as electric motors, household and office appliances, garden tools, electrical tools, power supplies, rectifiers, cable reels and power outlet strips.

Another feature of the thermal circuit breaker type 1120 is its positively trip-free mechanism which ensures reliable trip in the event of an overload even if the rocker should be jammed.

As type 1120 will often be placed in visually prominent places due to ist ON/OFF and protective function, an attractive styling has been chosen by Design. Rocker illumination is available upon request, reliably signalling the status of the device. In addition customer-specific designs of the housing front and the rocker as possible to ensure optimum integration in the base unit.

Of course circuit breaker type 1120 meets the requirements of the circuit breaker standards EN 60934 and UL 1077 and is therefore suitable for applications all over the world. Available voltage ratings are AC 240 V; AC 120 V; DC 28 V; DC 50 V, current ratings range from 3 to 16 A, for AC 120 V even up to 20 A.

Caption:

The rocker actuated circuit breaker type 1120 combines compact design with cost-effectiveness. (Foto: E-T-A)

E-T-A Elektrotechnische Apparate GmbH

In 2005 E-T-A Elektrotechnische Apparate GmbH achieved a turnover of €63m and had about 1300 people on the payroll worldwide. Production, Design, Market Research and Sales are concentrated at the headquarters in Altdorf. E-T-A’s major product line is circuit breakers for protection of electrical or electronic equipment against overload and short circuit. E-T-A manufactures thermal, thermal-magnetic, hydraulic-magnetic, purely magnetic and electronic circuit breakers including system solution featuring power distribution systems. A second product group covers electronic control products such as flow meters and monitors, level sensors, solid state remote power controllers and power relays. Customers for these products come from all kinds of industries, e.g. process control and automation, telecommunications, chemical and medical industry, manufacturers of household appliances and garden equipment, aerospace and marine industry.

For detailed information please visit E-T-A’s home page: www.e-t-a.com.

# Further information:

E-T-A Elektrotechnische Apparate GmbH

Thomas Weimann

Industriestr. 2 - 8

90518 Altdorf – Germany