#### PR292/pcb for 19BGT

# E-T-A exhibiting:

#### Hanover Fair 2007

Hall 11, booth B62

##### Printed circuit board is a fast and cost-effective solution for wiring racks

##### Ease of wiring

Altdorf, 10.3.2007 – E-T-A Elektrotechnische Apparate GmbH, sited in Altdorf near Nuremberg, offers a newly designed printed circuit board for their 19” rack 19BGT, representing a user-friendly and cost-effective wiring solution. Users in factory automation, chemical industry, pharmaceutical industry and telecommunications will profit by this addition to E-T-A’s product range of system solutions.

Up to now wiring of supply feed, auxiliary contacts, load outputs and various special functions had to be done individually and therefore was relatively time-consuming. Now the new pc board with integral terminal blocks offers fast and professional support with connection in control cabinets. The terminal blocks are soldered on to the pc board from the front side, on the rear side the pc board features integral terminals. Wiring of the rack becomes much more compact and may be carried out much faster. Risk of wiring errors is minimised.

An integral pull relief in the rack ensures resistance of the pc board against mechanical strain under harsh everyday conditions. The usual moveable wiring and its subsequent problems are thus excluded.

The pc board has been designed for single pole or double pole circuit breakers with max. 30 poles. This allows wiring up to 30 channels single pole, up to 15 channels double pole or twice 15 channels single pole redundantly for use with two separate circuits. A number of E-T-A overcurrent protection products may be used in connection with this printed circuit board: electronic circuit breaker type ESS20, electronic circuit protector ESX10, thermal-magnetic circuit breaker types 2210, 3600 and 3900, or the solid state remote power controller E-1048-700. Max. supply current is four times 50A, max. 20A are possible per load output.

Caption:

The newly designed printed circuit board for the 19“ rack 19BGT helps to reduce wiring time. (photo: E-T-A)

E-T-A Elektrotechnische Apparate GmbH

In 2006 E-T-A Elektrotechnische Apparate GmbH achieved a total turnover of €100m and had about 1400 people on the payroll worldwide. Production, Design, Market Research and Sales are concentrated at the headquarters in Altdorf.
E-T-A’s major product line consists of circuit breakers for protection of electrical or electronic equipment against overload and short circuit. E-T-A manufactures thermal, thermal-magnetic, hydraulic-magnetic, purely magnetic and electronic circuit breakers. Solid state remote power controllers are also part of E-T-A’s product portfolio. E-T-A serves almost every industry, e.g. process control and automation, telecommunications, chemical and medical industry, manufacturers of household appliances and garden equipment, aerospace and marine industry.

For detailed information please visit E-T-A’s home page: www.e-t-a.com.

# Further information:

E-T-A Elektrotechnische Apparate GmbH

Thomas Weimann

Industriestr. 2 - 8

90518 Altdorf – Germany

Phone: +49-9187-10227

Fax: +49-9187-10448

E-mail: thomas.weimann@e-t-a.de

www.e-t-a.com