#### PR293/X8345 High Current Power Distribution System for Control Cabinets

# E-T-A exhibiting

#### Hanover Fair 2007

Hall 11, booth B62

##### Compact and flexible power distribution system for mounting in control cabinets

##### Reliable and cost-effective power distribution in control cabinets

Altdorf, 10.3.2007 – E-T-A Elektrotechnische Apparate GmbH, located in Altdorf near Nuremberg, has launched a new power distribution model. Type 19BGT-X8345-S163 represents a new development for factory automation and process control as well as for the chemical and pharmaceutical industry. It has been designed for power supplies of control units programmable from memory and for sub-distribution of connected components such as sensors, actuators, bus systems, interfaces and other electronic components.

Type 19BGT-X8345-S163 combines lucidity of design with flexibility and modularity provided by plug-in type circuit breakers and with a high degree of operational safety through protection against brush contact provided by a moulded cover.

Supply feed from the side is max. 300 A, protection of the individual channels is by up to 18 E-T-A circuit breakers type 8345 with a max. current rating of 125 A per channel, ensuring greatest possible modularity. In order to provide protection against brush contact the power distribution system carries a plastic cover. Installation may be done directly on the mounting plate of the control cabinet.

Termination of the 19BGT-X8345-S163 is entirely carried out via reliable screw terminals and ring cable lugs. Integral auxiliary contacts for group signalisation may be connected from the side. The individual circuits are numbered, but may also be marked customer-specifically.

Caption:

The high current power distribution system 19BGT-X8345-S169 for a wide range of industrial applications combines flexibility with safe operation and clear design. (photo: E-T-A)

E-T-A Elektrotechnische Apparate GmbH

In 2006 E-T-A Elektrotechnische Apparate GmbH achieved a total turnover of €100m and had about 1400 people on the payroll worldwide. Production, Design, Market Research and Sales are concentrated at the headquarters in Altdorf.
E-T-A’s major product line consists of circuit breakers for protection of electrical or electronic equipment against overload and short circuit. E-T-A manufactures thermal, thermal-magnetic, hydraulic-magnetic, purely magnetic and electronic circuit breakers. Solid state remote power controllers are also part of E-T-A’s product portfolio. E-T-A serves almost every industry, e.g. process control and automation, telecommunications, chemical and medical industry, manufacturers of household appliances and garden equipment, aerospace and marine industry.

For detailed information please visit E-T-A’s home page: www.e-t-a.com.

# Further information:

E-T-A Elektrotechnische Apparate GmbH

Thomas Weimann

Industriestr. 2 - 8

90518 Altdorf – Germany

Phone: +49-9187-10227

Fax: +49-9187-10448

E-mail: thomas.weimann@e-t-a.de

www.e-t-a.com